## Slide 1
High Level Design Guideline
The Bootloader is intended to provide an easy means for loading applications from an external source. Instead of using a custom application via USB DFU or a FlashMagic, we want a nice “drag and drop” loader.
2.) This MSC bootloader will use an external flash device (SD card or serial NOR flash). When the device is plugged into the USB port, a drive will be enumerated. The data source will be an *external* flash device to the LPC43xx. Some of the other example code (say for the LPC17) emulatd a file system. Our filesystem will be *real* and external to the chip.
3.) The MSC bootloader will look for files on the external flash (i.e. Boot.hex) and use that file to program FLASH/RAM
4.) The bootloader should support intel hex files (i32 only). It would desirable for the bootloader to support .axf (.elf) files directly.
5.) The bootloader should be able to write both FLASH and RAM regions of the device. This will allow systems to boot from a SD card file to RAM.
6.) Allowed memory regions should be a compile time configuration to allow for other bootloader configurations.
7.) The bootloader should emit status messages over a UART for debugging. It should also be able to output to a graphics output (using eGFX Library).
8.) It would be desirable to get the application to fit in 128K of space
9.) Since we have an external file system, it would be possible for the user code to allow for network access for bootfiles
10.) Related to #9, if we can live with the extra code space, we could allow for a network drop of the code space in the bootloader.

## Slide 2
LPC43xx Bootloader Flow
Boot Entry
Init Boot Hardware
Check File System Sanity
Display File System Error
Check for new & valid boot image
Wait for File Copy Complete || Boot Button Pressed
Start USB Mass Storage Class Subsystem
Erase Target Memory
Program Target Memory
Rename Program Image with .prg extention [If programming internal flash]
Check for valid application in memory
Jump To User Application
Display Invalid Image Error
Display Critical Program/Erase Error
File System is not functional [drive not formatted, no disk, etc]
Wait for valid disk insertion, etc.
USB_MSC OK
No Valid User Application
No new file/image available
File exists but invalid [Incorrect format, invalid memory locations, etc]
File is valid
After 5 seconds
After 5 seconds
New file is loaded & boot button is pressed
File system is OK
1
2
3
4
5
6
7
8
9
10
12
13
14
15

## Slide 3
Common Bootloader I/O
BOOT_SWITCH - A button/IO used to trigger operations
STATUS_LED - Lowest level indication of status
UART - 115200 Baud connection to send out state/status during boot
eGFX [Optional] -Optional graphics subsystem for showing a user status/ progress bars
Bootloader Compile Time Configuration
Need a way to specify what the valid memory regions are for boot and what type of memory they are (FLASH, RAM, etc)
Need a way to specifying the access to the common I/O
So, for each application/board we will need a simple BSP file that supplies calls for the common IO